Case History

Industry		:	IT Sector

Project			:	CTS IT Park

Client			:	Larsen & Toubro Ltd.,

Location		:	Bantala, Dist 24 Parganas, West Bengal.

Completion Date	:	May 2009

Applicator		:	Unique Civitech Systems (P) Ltd., Chennai.

Products		:	NITOZINC PRIMER 		LOKFIX P

NITOBOND EP / AR		RENDEROC RG

RENDEROC S2		NITOWRAP 30						NITOWRAP 410		NITOWRAP CF

Area			:	500 Sq.Mtrs.

Project Value		:	39.00 Lacs.

Project Details		:	Larsen & Toubro had taken a turnkey project of an IT park for CTS located at Calcutta Leather Complex, Bantala, Dist 24 Parganas, West Bengal.

Due to some unknown reasons, there had been a fire accident in the ground floor level roof area which spread to an area of 350 Sq.Mtrs. The fire was extinguished within a short time and the building was not completed then. It was a PT slab with adequate reinforcements as per L&T design.

A preliminary destructive test of the core samples and non destructive tests were carried out through Jadhavpur University and was proposed to strengthen the roof.

Based on the inputs from Jadhavpur University reports and data from EDRC, FOSROC proposed a design for strengthening in different stages.

The design for strengthening of roof slab was studied by IIT Chennai and was also wetted by them.

Unique Civitech executed this job comprising of the below activities :

- Chipping of loose / damaged concrete mechanically,

- Providing & fixing of shear connectors / protective coating for rebars,

- Repair using Renderoc S2 for thickness upto 30 mm,

- Repair using Renderoc RG for thickness upto 60 mm by grouting from the top through core drills using positive displacement screw pumps,

- Carbon fibre wrapping – 1 & 2 layers as per design of IITC.

The strengthened surface was plastered using cement mortar as an additional precaution.

The work order was completed with a period of 1 month.

Post repair inspection was done by representative of IIT Chennai and has certified the same for quality as done as per specifications.

Before				 	After

Placing of Shuttering for Renderoc RG	Grouting of Renderoc RG using Pump

Carbon Fibre Wrapping – 2nd Layer		                 Completed Laminate